## Slide 1: Principles of Operation for Your Printer (and Others)

## Slide 2: Additive Manufacturing Techniques
There are lots of techniques for 3D Printing
But nearly all of them have in common a layer-based approach
  You print one layer at a time
    Top to bottom or bottom to top
  Depositing material in a single layer which takes the shape of the “slice” out of the overall geometry of the object that the layer intersects
  All layers together form an approximation of the complete geometry

## Slide 3: Additive Manufacturing Techniques
All of the layer based approaches have a critical property: Throughout the process there is a plane (usually horizontal) which completely separates what has already been printed (plus the current layer) from what will be printed in the future.
  If the print mechanism stays at or beyond the “unprinted” side that plane it is guaranteed to not hit the already printed material (as is a systemic problem with subtractive approaches that do not have this property)

## Slide 4: Another Common (But Not Universal) Aspect Between Technologies:
A Precision 3D Motion Platform
A precision motion platform is fairly easy to make
Several options, but most common involve use of 3 separate linear motion platforms ganged together
  Note: Most typically you have to move an entire motion platform with one of the other platforms (e.g., your X is moved by Z)
    Possible to avoid this, but there are drawbacks to those designs also

## Slide 5: Linear Motion Platform
Also not too difficult
  Most typical are timing belt (what you have for X and Y)
  or lead screw (your Z) drives
  Ratio of motor motion to linear motion tends to be smaller for lead screw compared to belt
    Slower but more precise
Motor / Drive

## Slide 6: Linear Motion Platform Related type of drive mechanism: “string” drive
Basically replace the belt with a string (often braided HPPE fibers – high tech fishing line)
Seems like it would slip but works remarkably well
If pulled very taught torque limit on motor is lower, so motor skips steps before line slips

## Slide 7: Linear Motion Platform
Also need something smooth to bear weight and translate across
  Rods and linear bearings
  Wheels on/in “track”

## Slide 8: Linear Motion Platform
Typical actuation by a stepper motor
  Open loop control
    Command a (precise) step and just assume it happened as commanded
Overall mechanism ends up simple
  Relationship between actuator & motion is simple
  Mechanism to transfer force is simple
   All the parts comparatively simple

## Slide 9: Considerations in Linear Motion Drive Mechanisms
Positional accuracy: minimum movement & repeatability
Hard to be more accurate than min movement size
Stepper motors: typically 200 steps / rotation (1.8°)
However modern stepper drive electronics can do partial steps (balances between steps)
As much as 16 “microsteps” for each step
But these are a little less accurate than full steps

## Slide 10: Considerations in Linear Motion Drive Mechanisms
Stepper motors: typically 200 steps / rotation (1.8°)
= 3200 µsteps / rotation
What this translates to in terms of linear motion depends on what amounts to the “gear ratio” of the drive mechanism.
Typical belt drive:
2mm tooth pitch on belt and 20 teeth on drive pulley
 40mm/rotation
 3200 µsteps/mm
 12.5 microns/µstep
rest of mech. probably not this precise, e.g., plastic deposition is typically ~400 microns (µm) wide
Typical lead screw: ~1-2mm/rotation so 20x more precise
(but also 20x slower)

## Slide 11: Considerations in Linear Motion Drive Mechanisms
Backlash
Originally seen in gears, but a form of it shows up in most drive mechanisms
Drive gear moves a tiny bit before contact tooth begins to push the next gear

## Slide 12: Considerations in Linear Motion Drive Mechanisms
Backlash
Originally seen in gears, but a form of it shows up in most drive mechanisms
Drive gear moves a tiny bit before contact tooth begins to push the next gear

## Slide 13: Considerations in Linear Motion Drive Mechanisms
Backlash
Originally seen in gears, but a form of it shows up in most drive mechanisms
Drive gear moves a tiny bit before contact tooth begins to push the next gear
This means the first bit of commanded motion is (sometimes) lost

## Slide 14: Considerations in Linear Motion Drive Mechanisms
Backlash
  Same thing happens for belt teeth and drive pulley teeth
  Very similar thing with threads on lead screw
With belt (and string) drive also have the effect of stretch in the belt
Important that your belts are tight (!) (slightly pre-stretched so first move isn’t taking up slack)
Also, can reduce this effect by slowing down
  Less velocity  less acceleration  less force

## Slide 15: Considerations in Linear Motion Drive Mechanisms
Avoiding Backlash
  Can we just make (e.g., gear teeth) exactly fit?

## Slide 16: Considerations in Linear Motion Drive Mechanisms
Avoiding Backlash
  Can we just make (e.g., gear teeth) exactly fit?
  Typically not: need space for lubrication and/or just too much wear and tear on the parts
One way to avoid is to always move in the same direction (Z-Axis does this!)

## Slide 17: Considerations in Linear Motion Drive Mechanisms
Avoiding Backlash
There are mechanisms to eliminate backlash but they are complicated (e.g., with recirculating balls in “Ball Screws”)
Mostly just try to minimize
   Keep your belts tight (note they will stretch a bit over time, but you will have a way to tighten them)

## Slide 18: Considerations in Linear Motion Drive Mechanisms
Other issues:
Rigidity and Squareness
Does the mechanism shift/bend slightly when it moves (e.g., rapidly)?
Is there a little “wiggle room” in mechanism?
Are the axes exactly 90° apart?
These are mostly determined by the printer design
BUT: make sure all your fasteners are fully tightened
Note: But you can be “too tight” and strip threads
Pay careful attention to bolts in stepper motors
(Hard) steel bolts in (softer) aluminum body

## Slide 19: Considerations in Linear Motion Drive Mechanisms
How do we know where we are?
With stepper motors we are counting the steps and always keep track of that (open loop control)
But when we power up (and a few other times) we may not know where we are counting from
Need a way to start: “end stops”
Homing: move towards end stop until switch closes, then we are at known position (e.g., 0)

## Slide 20: Another Kind of 3D Precision Motion Platform
Delta robot
  Three arms connected to create 3D platform
  (Video Demo: https://www.youtube.com/watch?v=v9oeOYMRvuQ)

## Slide 21: Another Kind of 3D Precision Motion Platform
Delta robot
  Can be very fast but can’t carry heavy loads
 Delta Printer
  For FDM 3D printer normally separate filament drive (with heavy motor) from hot end by pushing filament down a somewhat stiff tube: “Bowden tube”

## Slide 22
In addition to precision motion platform we also need a means to add/deposit material
This is where we see a lot of variations

## Slide 23: Additive Manufacturing Techniques FDM (Fused Deposition Modeling)
Your machine will be using FDM printing
  Sometimes called FFF (Fused Filament Fabrication)
  Developed by Scott Crump in the late 80’s who founded StrataSys where the idea was commercialized
Based on putting down layer via a thin bead of “melted” plastic which fuses with the layer below it
  Typically trace perimeter then do some pattern to (partially) fill the middle

## Slide 24: FDM Has Caught on Because it’s Relatively Easy to Build
Hard part in most printing tech is the deposition mechanism
For FDM you have two parts:
Hot end to heat and melt filament so it can be extruded out small orifice
Feed mechanism to push filament into hot end
    Solid filament acts as a piston to push melted filament out

## Slide 25: FDM Has Caught on Because it’s Relatively Easy to Build
Hard part in most printing tech is the deposition mechanism
Mechanically simple, but…
  Note that this requires that part of the filament below the drive stay solid (cold zone),
  but part near the end to always be molten (hot zone)
  Actually a rather tricky thermal balance here
    Heat can creep up the shaft and melt too high
    Fast moving filament can cause solid filament to hit bottom

## Slide 26
Other Types of Deposition for 3D Printing

## Slide 27: Additive Manufacturing Techniques Photopolymer Resin Based
Several techniques use a photopolymer resin
  Liquid resin (monomer)
  Catalyzed to bond in polymer chains by sufficiently energetic light (usually UV)
First 3D printing technique: Stereo Lithography (SLA)
Invented by Chuck Hull in 1986 who founded 3D Systems to commercialize

## Slide 28: Stereo Lithography
Scanning (UV) laser traces each layer on top of vat of photopolymer resin
Platform holding part is lowered after each layer allowing a new layer of resin on top
http://youtu.be/NM55ct5KwiI?t=44s

## Slide 29: Stereo Lithography Variations
Can also print at bottom and pull part upward
Can expose a whole layer at a time (instead of moving single point of laser around) using a projector (e.g., project a UV light image using a DLP projector)
http://youtu.be/snOErpOP5Xk?t=1m7s

## Slide 30: New Resin-Based Process: the Carbon3D Printer
A DLP-style photopolymer printer, but with substantially different chemistry
Much faster prints
Essentially no detectable layers
  no anisotropic (directional) material properties
New and better materials
https://www.youtube.com/watch?v=VTJq9Z5g4Jk&t=0.1

## Slide 31: Stereo Lithography
Disadvantages
  Messy
    Uncured resin is a bit toxic
  Until recently materials were pretty limited
    Somewhat brittle translucent plastic
    But starting to see new materials here (e.g., flexible)
  Intrinsically single material
    No separate support possible
But
  Can be very high resolution

## Slide 32: Another Resin Based Approach: “PolyJet” (by Objet, now StrataSys)
Use inkjet printer style heads to deposit very small droplets of photopolymer resin (16µm layer height)
Immediately cure in place with UV light
Trim layer to exact height with cutting blades
Repeat
http://youtu.be/MVo_IAd6Rwo?t=53s

## Slide 33: Another Resin Based Approach: “PolyJet” (by Objet, now StrataSys)
Multiple print heads can print different materials
  Including rather unique ones (flexible & transparent)
  Including support material
AND mix them at the droplet level
Can generate mixed materials with varying properties e.g., mix hard and flexible to vary stiffness at different locations within a single print
Also just started supporting mixing colored resins
Disadvantage: Presently expensive (printer & materials)

## Slide 34: Sintering Approaches
“Sintering” is fusing a powdered material to create a solid
A number of possible materials:
  metals, ceramic, plastic, sugar
Fusing normally done with heat, often laser
  “Selective Laser Sintering” (SLS)
Print starts with a bed of powder
  Heat parts that you want to be part of result (1 layer)
  Lower part and/or put another layer of power on bed
  Repeat http://youtu.be/wD9-QEo-qDk?t=1m47s

## Slide 35: Sintering Approaches
Single material, but powder provides intrinsic support
Variation
Can also fuse by applying an adhesive
E.g., inkjet print “superglue” (at high resolution)
Z-Corp (now 3D Systems) printers do this on gypsum powder
Also inkjet colored ink into powder
   full color result object
  http://youtu.be/BjBSoykoBNg?t=21s

## Slide 36: Layered Object Manufacturing (LOM)
Cut a material in profile(s) of layer
Bond to previous layers
Repeat
Note: can leave “waste” material in place to serve as support

## Slide 37: Layered Object Manufacturing (LOM)
First printers (and most common now) used paper
see: mcor technologies (http://mcortechnologies.com/)
(Video: http://youtu.be/TjDib7J3Iy4?t=1m40s)
Newest printers use inkjet on paper first to get full color objects
Also interesting approach for metal
  Thin sheets bonded with ultrasonic welding (See http://goo.gl/ifu0hN)

## Slide 38: Materials for Your Printer
Print with a thermoplastic
Comes in the form of a wire-like “filament”
For your printer: 1.75mm diameter filament
You have an allocation of ½ Kg (½ spool) from bulk order.

## Slide 39: Materials for Your Printer
You will normally print in PLA (“Polylactic Acid”)
Thermoplastic made from corn starch
  A type of polyester
  Biodegradable
  Non-toxic / biocompatible
  Quite well behaved
  Fairly “sticky”
  Comparatively low coefficient of thermal expansion (does not tend to warp and pull off of print bed)

## Slide 40: Materials for Your Printer
One health issue to be aware of:
  All FDM 3D printing produces ultra-fine “nano-particles” (smaller than 10 nanometers)
  Health effects not fully understood, but small particles are harder for body to get out of lungs
3D printing has similar emission rates (quantity of particles) as: cooking, burning scented candles, laser printer, burning cigarette
(see: http://spectrum.ieee.org/nanoclast/semiconductors/nanotechnology/nanoparticles-emitted-from-3d-printers-could-pose-a-risk http://www.sciencedirect.com/science/article/pii/S1352231013005086 )
PLA particles are at least bio compatible
But should probably still use in ventilated area

## Slide 41: Materials for Your Printer
Other major material for this type of printer: ABS
Acrylonitrile butadiene styrene
Better material properties than PLA
  A bit more ductile / less brittle
But harder to work with due to higher coefficient of thermal expansion
  Uneven cooling leads to warping and pulling up from bed
  Generally need a heated print bed to work consistently

## Slide 42: Materials for Your Printer
Other major material for this type of printer: ABS
Acrylonitrile butadiene styrene
Toxicity not completely clear:
  Hardened ABS is definitely non-toxic
  Fumes during printing, not as clear
  Monomer precursors are slightly carcinogenic (but not normally left in the polymer)
Ventilation should definitely be used

## Slide 43: Other Available Materials: Thermoplastics With Special Appearance
Wood (Laywoo-D3)
Wood particles embedded in a thermoplastic binder

## Slide 44: New Materials: Thermoplastics With Special Appearance
“Stone”(ish) (LayBrick)
Really just rough surface texture

## Slide 45: Other Materials: Thermoplastics With Special Appearance
Bronze/copper surface appearance
(ColorFabb bonzeFill & copperFill)
Metal particles in thermoplastic
When surface is sanded and polished plastic goes, metal stays

## Slide 46: Other Materials Conductive Filament
PLA with graphene in it
http://www.blackmagic3d.com/product-p/grphn-175.htm
Spec’d at 0.6Ω/cm
Currently very expensive
  $55 for 100g (Pure silver currently $61 for 100g)
Additional products about to hit the market

## Slide 47: Other Thermoplastics
PVA (Poly Vinyl Alcohol)
  Dissolves in water (support material)
  Tends to be hard to work with (must be kept very dry)
Nylon
Polycarbonate
High Impact Polystyrene (HIPS)
High Tensile Polyester

## Slide 48: Other Materials: Transparent
  (Sort of) for FDM with T-Glase filament from Taulman 3D (http://taulman3d.org/)

## Slide 49: Other Materials: Transparent
  (Sort of) for FDM with T-Glase filament from Taulman 3D (http://taulman3d.org/)
  More typical results:

## Slide 50: Other Materials: Flexible
Not everything should be made out of hard plastic
Several options for softer material
For FDM: “NinjaFlex” filament (http://www.ninjaflex3d.com/)
Must have an enclosed path from filament drive to top of hot end or it is too flexible to push through
Also doesn’t work with Bowden drive

## Slide 51: Aside: Things to Look at When Considering Exotic FDM Filaments
Odor and possible toxicity :
  PLA is about the best, others at a minimum smell a bit and could be somewhat toxic Nylon is apparently particularly bad / toxic
Coefficient of thermal expansion, but really “do you need a heated print bed?”
Temperature for extrusion
Reports of whether it’s “hard to work with”